## Slide 1
COVESA ALL MEMBER MEETING
Vehicle Capabilities
A runnable power-window reference example
01
Semantic intent
02
Stable API boundaries
03
Executable models
COVESA All Member Meeting | Window capability reference example
01 / 14
Notes: Timing: 00:00-00:45 (45 seconds)
Introduce the talk as a reference example and a discussion proposal, not an adopted COVESA standard. We will follow one window command from an application to a simulated motor. The goal is to make interfaces and behavior concrete enough for members to challenge and improve. Add the approved presenter name and meeting date before presenting.

## Slide 2
THE PROBLEM
Applications Need Intent, Not Wiring
Move the window to 75% open, without knowing the motor driver.
01
Signals describe values
02
Transport APIs describe access
03
Capabilities describe behavior
COVESA All Member Meeting | Window capability reference example
02 / 14
Notes: Timing: 00:45-02:00 (75 seconds)
A window is deliberately ordinary. An application should not need a bus identifier, supplier pinout, or ECU address to request a position. A transport API alone does not settle ownership, inhibition, completion, or failure semantics. A capability is the place to give that request a domain meaning. This complements signal-level interoperability rather than replacing it.

## Slide 3
SCOPE
A Small, Deliberate Reference Scope
One implemented capability. Enough surrounding structure to run it.
01
Power windows: four semantic zones
02
HTTP adapter, catalog and explorer
03
Simulator binding and motor model
Vehicle state and power management are platform stand-ins, not production services.
COVESA All Member Meeting | Window capability reference example
03 / 14
Notes: Timing: 02:00-03:30 (90 seconds)
The runnable scope is windows only. Other domains in the architectural picture are context, not released capability implementations. The composition root wires the bus, vehicle-state stub, simulator, manager, and window orchestrator. A power stub is present but the manager does not request power authorization. Do not imply that this example implements the full vehicle architecture.

## Slide 4
ARCHITECTURE
Two Boundaries, One Capability
Separate caller intent from deployment-specific actuation.
Application / HMI
Northbound API
Window capability
Southbound port
Simulator + motor model
Intent flows down
Position + typed state return
Hardware addresses stay below the port
COVESA All Member Meeting | Window capability reference example
04 / 14
Notes: Timing: 03:30-05:30 (120 seconds)
Read the diagram top to bottom. The northbound API accepts semantic commands and returns typed state. The manager owns domain gates and dispatch. The southbound port exposes abstract actuation and position read-back. The simulator is the implemented binding; a hardware binding is a future integration point. Deployment addressing remains below the port. State events provide feedback to callers. These boundaries are architectural contracts, not necessarily process or network boundaries.

## Slide 5
NORTHBOUND
The Northbound Contract
What callers ask for, and what they can reason about.
01
Move: zone + target + request identity
02
Preflight and explicit release
03
State: position, status and typed reason
API convention: 0% = closed; 100% = open.
COVESA All Member Meeting | Window capability reference example
05 / 14
Notes: Timing: 05:30-07:00 (90 seconds)
Describe MoveWindowCommand and WindowState. The adapter derives the request source from its configured role and rejects a source field in the payload. That is a demonstration configuration, not a credential verification system. Runtime endpoints are under /vehicle/window. The checked-in OpenAPI paths and response codes currently differ from the adapter and need alignment before consumers generate clients. Avoid presenting that drift as a standardized contract.

## Slide 6
BEHAVIOR
A Request Has Five Phases
Make execution order visible and inspectable.
01
Arbitrate
02
Precondition
03
Safety checks
04
Actuate
05
Publish
COVESA All Member Meeting | Window capability reference example
06 / 14
Notes: Timing: 07:00-08:30 (90 seconds)
The manager executes arbitration, preconditions, safety checks, actuator dispatch, and state publication. Current gates check power OFF, OTA activity, undervoltage, and target range. Timeout and explicit release use cancellation and position read-back support. The term safety checks is not an ISO 26262 safety case or certification claim. Priority logic exists, but the manager holds one lock throughout a move, so immediate priority preemption and independent zone concurrency should not be claimed as proven. The explorer's phase replay is an explanatory animation, not live execution tracing.

## Slide 7
SOUTHBOUND
The Southbound Contract
A binding changes; the caller's vocabulary does not.
01
move_window(zone, target_pct)
02
get_window_position(zone)
03
describe_actuator(capability)
Timeout or release requires a binding that can stop safely on cancellation.
COVESA All Member Meeting | Window capability reference example
07 / 14
Notes: Timing: 08:30-10:00 (90 seconds)
The WindowActuatorPort is an abstract interface. The simulator maps API percentages to model millimeters and reports the resulting position. A deployment profile describes electrical, travel, load, and geometry quantities without hardware addresses. A real binding would implement transport and feedback. The simulator runs physics synchronously inside its async method, so it is not evidence of interruptible hardware timing. No real ECU integration is demonstrated here.

## Slide 8
MODEL
An Executable Plant Model
Connect interface intent to physical behavior.
01
DC motor
02
Actuator
03
Linkage
04
Window load
Simulated KPIs: move latency, current, force, travel and energy.
COVESA All Member Meeting | Window capability reference example
08 / 14
Notes: Timing: 10:00-11:30 (90 seconds)
Explain the four-stage bond-graph representation: electrical drive and motor, rotary-to-linear actuation, linkage, and window load. The model can generate a trajectory, compute KPIs, and respond to an imposed obstruction in model-level tests. Model position is the opposite of API openness: 0 mm is open and 300 mm is closed for the default model. Parameters and outputs are illustrative simulation data, not measured supplier specifications or vehicle validation evidence. No production anti-pinch timing guarantee is established.

## Slide 9
COVESA ALIGNMENT
Capabilities Complement VSS
Keep signal references, behavior and deployment separate.
01
Signal reference: VSS position path
02
Behavior: MoveWindowCommand / WindowState
03
Deployment: actuator binding and profile
Vehicle.Cabin.Door.Row1.DriverSide.Window.Position
COVESA All Member Meeting | Window capability reference example
09 / 14
Notes: Timing: 11:30-13:00 (90 seconds)
VSS supplies a shared signal vocabulary. The example attaches VSS paths to capability metadata and relevant operations, while defining command and result semantics separately. This is VSS-referenced metadata, not a demonstrated VSS server integration or a conformance certification. Agreeing units, ranges, and direction conventions is essential; review the exact mapping against the chosen VSS release. The catalog can help discover interfaces and model parameters without embedding transport addresses.

## Slide 10
LIVE DEMO
Demo: Follow One Window Command
Three minutes: discover, explain, execute, inspect.
01
Catalog: select Window Movement Control
02
Boundary: step through the phases
03
Explorer: move to 75% and inspect state
Local demo: http://127.0.0.1:8770/vehicle/catalog/
COVESA All Member Meeting | Window capability reference example
10 / 14
Notes: Timing: 13:00-16:00 (180 seconds)
0:00-0:30: Open http://127.0.0.1:8770/vehicle/catalog/?cap=window&tab=overview and show the descriptor and ports. 0:30-1:15: Open ?cap=window&tab=boundary, choose a move operation, and step through the explanatory replay. State explicitly that replay is not live instrumentation. 1:15-2:00: Open ?main_tab=explorer, choose DRIVER_FRONT and 75%, execute, then show the response and event log. The configured adapter role controls source; do not rely on a selector to switch identity. 2:00-3:00: Open /vehicle/api-explorer/ and show the physics playground trajectory and KPIs. Explain that playground simulation is a separate model run, not motor telemetry. If the demo is unavailable, use the deck's architecture and pipeline diagrams and the following HTTP fallback: POST /vehicle/window/move with {"zone":"DRIVER_FRONT","target_pct":75}; GET /vehicle/window/state?zone=DRIVER_FRONT. Rehearse on the actual machine first. Start using python -m capability_framework.app --no-browser.

## Slide 11
EVIDENCE
What The Example Demonstrates
Concrete evidence, without overstating readiness.
01
Runnable HTTP-to-simulator path
02
Tests for model, API and explorer
03
Introspectable interfaces and model
Not demonstrated: real hardware, certified safety or production authentication.
COVESA All Member Meeting | Window capability reference example
11 / 14
Notes: Timing: 16:00-17:30 (90 seconds)
The repository has tests for target movement, model KPIs, obstruction detection, power-off inhibition, HTTP operations, catalog rendering, diagrams, and playground simulation. These establish behavior within a reference example, not production readiness. Do not cite a test count without running the checked-out revision. The window orchestrator issues manager commands sequentially even for its SYNC convenience mode. The runtime returns MOVING after its simulated call completes; completion and status semantics remain a collaboration question. Calibration profile types exist, but automatic outcome reporting is not wired in the current main revision.

## Slide 12
DISCUSSION PROPOSAL
Candidate Topics For Collaboration
Agree behavior at the boundaries before prescribing deployment.
01
Command lifecycle and completion semantics
02
Cancellation, ownership and typed failures
03
Port contracts, units and VSS mappings
COVESA All Member Meeting | Window capability reference example
12 / 14
Notes: Timing: 17:30-18:30 (60 seconds)
Present these as candidate topics for member discussion. No adopted standard or workgroup commitment is implied. Which elements should be portable across deployments? How should asynchronous completion and state observation work? What must a binding guarantee on cancellation? What verification examples should accompany a contract? Keep transport choices and hardware topology as extension concerns unless members identify a compelling interoperability need.

## Slide 13
NEXT STEPS
From Reference To Shared Artifact
Small scope, explicit gaps, repeatable review.
01
Align contract, catalog and runtime
02
Add conformance and fault-injection cases
03
Review provenance and publication approval
COVESA All Member Meeting | Window capability reference example
13 / 14
Notes: Timing: 18:30-19:30 (60 seconds)
Propose a practical sequence. First align the OpenAPI paths, statuses, and schemas with runtime behavior. Then exercise arbitration, interruptibility, cancellation, fault reporting, and model limits. Validate a second binding before claiming hardware portability. Publication requires the owner's review of code and parameter provenance, copyright permissions, and licensing. The repository LICENSE is currently a placeholder while package metadata declares Apache-2.0; this must be reconciled. A keyword scan cannot establish absence of proprietary information. The deck avoids employee names, internal repositories, and internal rule identifiers, but remains subject to release review.

## Slide 14
DISCUSSION
Which Boundary Should We Agree First?
One window. Two interfaces. A concrete starting point.
01
Caller semantics
02
Binding guarantees
03
Verification evidence
COVESA All Member Meeting | Window capability reference example
14 / 14
Notes: Timing: 19:30-20:00 (30 seconds)
Close with the central invitation: use this small runnable example to decide which boundary semantics deserve shared agreement. Ask members to nominate one missing guarantee, one binding scenario, or one verification case. The planned talk is 20 minutes including the demo; any extended questions need additional agenda time. Do not announce a public repository link until publication is approved.